## Slide 1: Microblaze Implementation of a Multicolored LED Control System
Justin Bui

## Slide 2: Agenda
Project introduction
Inspiration
HDL Development
C++ Development
Potential Future Implementations

## Slide 3: Project Introduction
Control System for the Nexys 4 DDR RGB LEDs
Features:
  Each LED is controlled Independently
  100MHz Update (Rapid Response)
  Easy To Use Set and Clear Commands

## Slide 4: Inspiration
Experience developing boards with LED indicators
  Communications (strobe)
  Power Indicators (Charge status, on/off indicators, etc.)
LEDs can be used to communicate Error codes for Field Troubleshooting
  Communications Errors (i.e. baud rate mismatch, etc.)
  Power Quality Issues (low voltage, burnt fuse, etc.)

## Slide 5: HDL Development
Individual LED Object
  4 Inputs, 1 3bit Output per LED element
    Clock, Red, Green, and Blue input signals
    Mled [2:0] output vector
Core and Wrapper
  Single Register Implementation
    1 Byte for MLED0, 1 Byte for MLED1
    One bit per color (bits 2 – 0)
  No Data Returned

## Slide 6: C++ Development
mLED Class
  Set and Clear Functions for All colors
    UINT8_T passed to indicate which LED to “program”
  Read and Write functions (Register level)
Test File
  Toggle Red and Green on LED0, Blue on LED1, with variable hold times
  UART Communications for Status Tracking (via Terminal)

## Slide 7: Potential Implementations
PWM Based Intensity Control (dimmer)
  Allows for more complexity in colors
Error Coding
  Frequency Controlled strobing
  Color Changes/Variation
Communications
  UART/SPI Monitoring
Power Supply Monitoring
  Battery Charge, Low Voltage Monitoring, etc.